Ausschreibungstext

GreenLife Erdtank 6.500 l / GET 6.5 – Regenwassererdtank

Volumen:		6.500 l

Mögliche Anschlussgrößen: 	DN100

inkl. Schiebedom 450 mm – 695 mm stufenlos ausziehbar und 5° neigbar zur optimalen Geländeanpassung

Einstiegsöffnung 600 mm

inkl. Sicherheitskunststoffabdeckung 200 kg begehbar,

Kindersicher verschraubbar mit 2 Edelstahlschrauben

Option: 		PKW-befahrbar (bis 600 kg Achslast) – PKW-befahrbare Abdeckung (G0001240)

LKW-befahrbar (SLW 30) – Set für LKW-Befahrbarkeit (G0003335)

im Vergleich zu Beton einfacheres Handling – geringeres Gewicht

Optionale Ausstattungsvarianten erhältlich

Ausstattungsversion „Biovitor“:

Der Biovitor- der biologische Regenwasserfilter - perfekt dimensionierte Größenverhältnisse der Kammern und Durchlässe gewährleisten optimale biologische Abläufe mit höchstem Wirkungsgrad.

inklusive Biovitor DN 100 und Überlaufsiphon mit Tierschutz, Schiebedom mit Abdeckung (begehbar, aus Kunststoff), 3 Anschlüssen DN 100

Ausstattungsversion „Tankeinbaufilter“:

inklusive Tankeinbaufilter, Zulaufberuhiger und Überlaufsiphon mit Tierschutz, Schiebedom mit Abdeckung (begehbar, aus Kunststoff), 3 Anschlüssen DN 100

Ausstattungsversion „Einbaufilter“:

inklusive Einbaufilter, Zulaufberuhiger, Überlaufsiphon mit Tierschutz, Schiebedom mit Abdeckung (begehbar, aus Kunststoff), 3 Anschlüssen DN 100

Ausstattungsversion „Zulaufberuhiger“:

inklusive Zulaufberuhiger, Überlaufsiphon mit Tierschutz, Schiebedom mit Abdeckung (begehbar, aus Kunststoff), 3 Anschlüssen DN 100

Geeignet zur Lagerung von Regenwasser, häuslichen Abwässern, Betriebswasser.

Auch erhältlich als Schlammfang oder Leichtflüssigkeitsabscheider und zur Feuerlöschreserve.

Optionale Ausstattungsvarianten erhältlich

Auch als Retentionsbehälter erhältlich (die Retentionsdrossel ist nicht nachträglich einbaubar!)

15 Jahre Materialgarantie auf den Behälter!

Hohe Formstabilität durch dicke Wandstärken

UV-Beständigkeit für konstante Materialqualität.

Inhalt: 			6.500 l

Gewicht: 		260 kg

Material:		PE

Länge: 			2.300 mm

Breite:			2.100 mm

Höhe mit Dom: 		2.500 – 2.745 mm

Artikelnummer:	 	G0000291

Mengeneinheit:		Stück

Herstellerangaben:

GreenLife GmbH

Sacktannen 1a

19057 Schwerin

Telefon 	+49 (0) 385 – 77337-0

Telefax 	+49 (0) 385 – 77337-33

Web		www.greenlife.de

E-Mail		projects@greenlife.info

Menge: …………	Einheit: Stk.	EP: …………   GP: …………

Tender specification

GreenLife underground tank 6500 l / GET 6.5 – rainwater tank

volume:			6500 l

possible connection sizes:	DN100

incl. one telescopic dome 450 – 695 mm infinitely extendable and 5° tilt for optimized adaptation to terrain surface

access opening 600 mm (according DIN 1989) – for inspection purposes

incl. plastic safety cover (load capacity: 200 kg, walkable),

child-safe screwed – with 2 stainless steel screws

options:      accessible by cars (up to 600 kg axle load) – Kit accessible by cars (G0001724)

accessibility for trucks (class SLW 30) - kit for accessibility of trucks (G0003335)

easier handling in comparison to concrete shafts – lower weight

optional features available:

version with „Biovitor":

The Biovitor - the biological rainwater filter - perfectly dimensioned chambers and diffusers ensure optimal biological processes with maximum efficiency.

including Biovitor DN 100 and overflow siphon with animal protection, telescopic dome with cover (walkable, made of plastic), 3 DN 100 connections.

version "tank integral filter":

including tank integral filter, calmed inlet and overflow siphon with animal protection, telescopic dome with cover (walkable, made of plastic), 3 connections DN 100

version "garden filter":

including installation filter, calmed inlet, overflow siphon with animal protection, telescopic dome with cover (walkable, made of plastic), 3 connections DN 100

version „calmed inlet:

including calmed inlet, overflow siphon with animal protection, telescopic dome with cover (walkable, made of plastic), 3 DN 100 connections.

Suitable for the storage of rainwater, domestic waste water, process water.
Also available as sedimentation or light liquids separator and fire-fighting reserve.

Optional equipment versions available!
Even as retention tank available (retention throttle is retrofitted!)

15 years material warranty on the tanks/shafts!

Strong walls – best construction of GreenLife stability profiles

UV resistance for a constant material quality

volume:			6500 l

weight: 			260 kg

material: 		PE

length:			2300 mm

width:	 		2100 mm

height:			2500 – 2745 mm

item no.:	 	G0000291

unit of quantity:		piece

manufacturer:

GreenLife GmbH

Sacktannen 1a

D-19057 Schwerin

Germany

phone 		+49 (0) 385 – 77337-0

fax 		+49 (0) 385 – 77337-33

web		www.greenlife.de

e-mail		projects@greenlife.info

quantity: …………	unit: piece	single price: …………   total price: …………